Fundamental limitations and perspective of development

of quantum nanoelectronics

К.Yu. Arutyunov

Nanocenter of University of Jyvaskyla, 35, 40014, Jyvaskyla, Finland

Konstantin.Arutyunov@phys.jyu.fi

Over a number of last decades increase of integration by further miniaturization has been the tendency of electronics development [1]. One may ask a reasonable question: are there any fundamental limitations for the size reduction of electronic elements? Modern technology is capable of reproducible fabrication of nanostructures with sub-10 nm features [2,3]. At these scales various quantum size phenomena suppress electric conductivity in normal metals [4], reduce charge mobility in semiconductors [5] and lead to finite resistivity in superconductors [6-8]. All mentioned effects result in fundamental limitations on utilization of ultra-small elements in nanoelectronic circuits. However, the indicated size effects may lead to a new class of quantum logic [9], and can be used for various applications: for example – quantum standard of electric current [10].

[1] G. Moore, Electronics, 38, 8-13 (1965).

[2] M. Savolainen, V. Touboltsev, P. Koppinen, K.-P. Riikonen and K. Yu. Arutyunov, “Ion beam sputtering method for progressive reduction of nanostructures dimensions”, Appl. Phys. A 79, 1769-1773 (2004).

[3] M.Zgirski, K-P. Riikonen, V. Tuboltsev, P. Jalkanen, T. T. Hongisto and K. Yu. Arutyunov, “Ion beam shaping and downsizing of nanostructures”, Nanotechnology 19 055301-1 -  055301-6 (2008).

[4] K. Arutyunov, M. Zgirski, K.-P. Riikonen, and P. Jalkanen, “Quantum Limitations of Electron Transport in Ultra-Narrow Nanowires“, International Review of Physics (IREPHY) 1, 28-30 (2007).

[5] V. Fonoberov and A. Balandin, Nano Lett. 6, 2442 (2006).

[6] M. Zgirski, K.-P. Riikonen, V. Touboltsev, and K. Arutyunov, ”Size Dependent Breakdown of Superconductivity in Ultranarrow Nanowires”, Nano Lett. 5, 1029 (2005).

[7] M. Zgirski, K.-P. Riikonen, V. Touboltsev and K.Yu. Arutyunov, “Quantum fluctuations in ultranarrow superconducting nanowires”, Phys. Rev. B. 77, 054508-1 – 054508-6 (2008).

[8] K. Yu. Arutyunov, D. S. Golubev, and  A.D. Zaikin “Superconductivity in one dimension” Physics Reports 464, 1-70 (2008).

[9] J. E. Mooij and H. Haremans, New Journal of Physics 7, 219 (2005).

[10] J. E. Mooij and Yu. V. Nazarov, Nature Physics 2, 169 (2006).